## Slide 1: Grid and Market Modelling (BEIS Study)
EPSRC Grid Scale Energy Storage

## Slide 2: The GB Transmission Network
Built starting from the National Grid Electricity Ten-Year Statement 2021, and adding the lines planned in 2022
Some information:
2934 lines from 400 kV to 33 kV
38 extra lines
2020 nodes

## Slide 3: Generators and Consumers
+50 MW in England and Wales
+30 MW in South Scotland
+10 MW in North Scotland
Submit the expected generation and demand for each 30 minutes settlement period to ESO with a time resolution of one minute
Gen. and Dem.
Elexon, 2020a. Balancing and Settlement Code. https://www.elexon.co.uk/bsc-and-codes/balancing-settlement-code/.

## Slide 4
FPNs
Expected Generation Imbalance
Expected Demand Imbalance
NG ESO
Power Injections at Each Node
offer and bid orders to increase and decrease power injections, respectively
Solve:
Transmission Line Constraint Violation and Offset Energy Imbalance

## Slide 5: Bid and Offer Orders
Unit
up to five bid orders and five offer orders
Settlement Period
Wind and Solar Power Plants
(Marginal Costs≈0)
/MWh
Subsidy
(renewables obligation certificates or a strike price in a CfD)
(negative) bid price equal to the value of the lost subsidy
compensation for curtailed power

## Slide 6: Balancing Mechanism Model
Modelling of the BM rebalancing costs
Minimization (Offer Cost - Bid Cost)
Offer Cost = the system operator has to pay to the unit 𝑘 to increase its power
Bid Cost = the unit 𝑘 has to pay to the system operator to reduce the power
Constraints: - power output of the unit 𝑘
- power balance at node 𝑛 and time 𝑡
- power flow over the lines
- minimum and maximum flows for transmission lines
- minimum and maximum capacity limits of each unit
- upper bounds for each offer and bid order

## Slide 7: Mathematical Description

## Slide 8: Type of technology and percentage of identified marginal units
August 2020 and January 2021

## Slide 9: Carbon emission intensity of different technologies

## Slide 10: Case study: +1 MW renewable generation in different regions in GB -1 MW from marginal units
Additional BM costs for managing congestions
Total carbon abatement
Savelli, I., Hardy, J., Hepburn, C., & Morstyn, T. (2022). Putting wind and solar in their place: Internalising congestion and other system-wide costs with enhanced contracts for difference in Great Britain. Energy Economics, 113, 106218.

## Slide 11: Challenges with embedded units (1)
For directly connected units (generators and large loads) we have the exact connection point.
E.g.
Name | ETYS Node
Drax | DRAX41
For demand and embedded generation, we only have the DNO area
E.g.

## Slide 12: Challenges with embedded units (2)
Embedded unit data:
Scheduled dem./gen.
Loss factor
Up/Down bids
DNO area
Demand in each Grid Supply Point (GSP)
Future Energy Scenario (National Grid)
% Demand in each GSP
A better solution?
Our approach:
Total demand in each DNO area

## Slide 13: Future Extension Work
Some energy storage capacities (could be in different technologies)
Σ
Assessment of congestion cost during the rebalancing action
Evaluate the carbon emission during the rebalancing action
?

## Slide 14
Thank You for Your Attention
Any Question?